Juniper EX 4200 Switch
1. Connet serial console cable to Com port in the back of the switch.
2. Plug in Patch cable to management ethernet port in the back of the switch.
3. Connect the patch cable to the management device.
4. Install a open source TFTP server ( Solar winds for example)
5. Go into you device manager , Net work devices and disable the firewall settings and the wifi card on the computer.
6. In network devices:
   -	Right click ethernet adaptor
   -	Go down to properties
   -	Scroll down tell you see IPV4 and double click
   -	Click manually assign a IP address , fill in the fields up to the default gateway.
7. Install a consle program on the management device (Putty)
8. Connect the serial console cable to the computer with a usb > serial adapter or just serial if the computer has it.
9. Check the COM port in device manager, make sure they match in putty. Bod rate can be left on the default setting.
10. With the CLI loading on the switch hit SPACE or ENTER tell you see LOADER >
11. Enter the following commands:
- loader> set ipaddr=192.168.100.2
-loader> set netmask=255.255.255.0
-loader> set gatewayip=192.168.100.254
-loader> set serverip=192.168.100.1
-loader> install --format tftp://<tftp server>/<Junos package name>
For example: loader> install --format tftp://192.168.100.1/jinstall-ex-4200-15.1R7-S6.3-domestic-signed.tgz
*Make sure to have the Jonos os file in the root directory for the TFTP server.